## Slide 1: Computer Architecture and Logic Design (CALD) Lecture 14
+

## Slide 2: Analysis of Clocked Sequential Circuits

## Slide 3: Analysis of Clocked Sequential Circuits
+
Example
A B = 0 0
D Q
Q
CLK
D Q
Q
A
B
y
The State
  State = Values of all Flip-Flops
x
Eastern Mediterranean University

## Slide 4: Analysis of Clocked Sequential
+
D Q
Q
CLK
D Q
Q
Circuits
State Equations
A(t+1) = D
Eastern Mediterranean University
A
B
y
x
A
= A(t) x(t)+B(t) x(t)
= A x + B x B(t+1) = DB
= A’(t) x(t)
= A’ x
= [A(t)+ B(t)] x’(t)
= (A + B) x’
y(t)

## Slide 5: Analysis of Clocked Sequential
+
Circuits
State Table (Transition Table)
D Q
Q
CLK
D Q
Q
A
B
y
x
A(t+1) = A x + B x B(t+1) = A’ x
Present State |  |  |  | Input | Next State |  | Output
 | A | B |  | x | A | B | y
 | 0 | 0 |  | 0 | 0 0 |  | 0
 | 0 | 0 |  | 1 | 0 1 |  | 0
 | 0 | 1 |  | 0 | 0 0 |  | 1
 | 0 | 1 |  | 1 | 1 1 |  | 0
 | 1 | 0 |  | 0 | 0 0 |  | 1
 | 1 | 0 |  | 1 | 1 0 |  | 0
 | 1 | 1 |  | 0 | 0 0 |  | 1
 | 1 | 1 |  | 1 | 1 0 |  | 0
y(t)
= (A + B) x’
t
t+1
t
Eastern Mediterranean University

## Slide 6: Analysis of Clocked Sequential
+
Circuits
State Table (Transition Table)
D Q
Q
CLK
D Q
Q
A
B
y
x
A(t+1) = A x + B x B(t+1) = A’ x
Present State |  | Next State |  |  |  | Output | 
 |  | x = 0 |  | x = 1 |  | x = 0 | x = 1
A | B | A | B | A | B | y | y
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
t+1
t
t
y(t)
= (A + B) x’
Eastern Mediterranean University

## Slide 7: Analysis of Clocked Sequential
Circuits
State Diagram
Present State |  | Next State |  |  |  | Output | 
 |  | x = 0 |  | x = 1 |  | x = 0 | x = 1
A | B | A | B | A | B | y | y
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
Eastern Mediterranean
D Q
Q
CLK
D Q
Q
A
B
y
x
0 0
1 0
0 1
1 1
0/0
0/1
1/0
1/0
1/0
1/0
0/1
0/1
AB
input/output

## Slide 8: Analysis of Clocked Sequential Circuits
+
D Flip-Flops
Example:
D Q
Q
x
CLK
y
A
Present State | Input |  | Next State
A | x | y | A
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
0
1
00,11
Eastern Mediterranean University
00,11
A(t+1) = DA = A  x  y
01,10
01,10

## Slide 9: Analysis of Clocked Sequential Circuits
+
JK Flip-Flops
Example:
J Q
K Q
CLK
x
Eastern Mediterranean University
Q A
Q
B
JA = B JB = x’
KA = B x’
KB = A  x
A(t+1) = JA Q’A + K’A QA
= A’B + AB’ + Ax
B(t+1) = JB Q’B + K’B QB
= B’x’ + ABx + A’Bx’
Present State |  | I/P | Next State |  | Flip-Flop Inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 | 0 1 |  | 0 0 |  | 1 0 | 
0 | 0 | 1 | 0 0 |  | 0 0 |  | 0 1 | 
0 | 1 | 0 | 1 1 |  | 1 1 |  | 1 0 | 
0 | 1 | 1 | 1 0 |  | 1 0 |  | 0 1 | 
1 | 0 | 0 | 1 1 |  | 0 0 |  | 1 1 | 
1 | 0 | 1 | 1 0 |  | 0 0 |  | 0 0 | 
1 | 1 | 0 | 0 0 |  | 1 1 |  | 1 1 | 
1 | 1 | 1 | 1 1 |  | 1 0 |  | 0 0 | 

## Slide 10: Analysis of Clocked Sequential Circuits
+
JK Flip-Flops
Example:
J Q
K Q
CLK
x
Q A
Q
B
Present State |  | I/P | Next State |  | Flip-Flop Inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 | 0 1 |  | 0 0 |  | 1 0 | 
0 | 0 | 1 | 0 0 |  | 0 0 |  | 0 1 | 
0 | 1 | 0 | 1 1 |  | 1 1 |  | 1 0 | 
0 | 1 | 1 | 1 0 |  | 1 0 |  | 0 1 | 
1 | 0 | 0 | 1 1 |  | 0 0 |  | 1 1 | 
1 | 0 | 1 | 1 0 |  | 0 0 |  | 0 0 | 
1 | 1 | 0 | 0 0 |  | 1 1 |  | 1 1 | 
1 | 1 | 1 | 1 1 |  | 1 0 |  | 0 0 | 
0 0
1
1
Eastern Mediterranean University
1 1
0 1
1 0
1
0
1
0
0
0

## Slide 11: Analysis of Clocked Sequential Circuits
+
T Flip-Flops
Example:
Eastern Mediterranean University
T = B x
A
y = A B
B
T = x
A(t+1) = TA Q’A + T’A QA
= AB’ + Ax’ + A’Bx
B(t+1) = TB Q’B + T’B QB
= x  B
T
Q A
Q
R
T Q
B
Q
R
CLK
Reset
x
y
Present State |  | I/P | Next State |  | F.F Inputs |  | O/P
A | B | x | A | B | TA | TB | y
0 | 0 | 0 | 0 0 |  | 0 | 0 | 0
0 | 0 | 1 | 0 1 |  | 0 | 1 | 0
0 | 1 | 0 | 0 1 |  | 0 | 0 | 0
0 | 1 | 1 | 1 0 |  | 1 | 1 | 0
1 | 0 | 0 | 1 0 |  | 0 | 0 | 0
1 | 0 | 1 | 1 1 |  | 0 | 1 | 0
1 | 1 | 0 | 1 1 |  | 0 | 0 | 1
1 | 1 | 1 | 0 0 |  | 1 | 1 | 1

## Slide 12: Analysis of Clocked Sequential Circuits
+
T Flip-Flops
Example:
Eastern Mediterranean University
A
T Q
Q
R
T Q
B
Q
R
CLK
Reset
x
y
Present State |  | I/P | Next State |  | F.F Inputs |  | O/P
A | B | x | A | B | TA | TB | y
0 | 0 | 0 | 0 0 |  | 0 | 0 | 0
0 | 0 | 1 | 0 1 |  | 0 | 1 | 0
0 | 1 | 0 | 0 1 |  | 0 | 0 | 0
0 | 1 | 1 | 1 0 |  | 1 | 1 | 0
1 | 0 | 0 | 1 0 |  | 0 | 0 | 0
1 | 0 | 1 | 1 1 |  | 0 | 1 | 0
1 | 1 | 0 | 1 1 |  | 0 | 0 | 1
1 | 1 | 1 | 0 0 |  | 1 | 1 | 1
0 0
0 1
1 1
1 0
0/0
1/0
0/0
1/0
1/0
1/1
0/0
0/1