## Slide 1: Computer Architecture and Logic Design (CALD) Lecture 03

## Slide 2: Computer Function and Interconnection

## Slide 3: Computer Components
Contemporary computer designs are based on concepts developed by John von Neumann at the Institute for Advanced Studies, Princeton
Referred to as the von Neumann architecture and is based on three key concepts:
  Data and instructions are stored in a single read-write memory
  The contents of this memory are addressable by location, without regard to the type of data contained there
  Execution occurs in a sequential fashion (unless explicitly modified) from one instruction to the next
Hardwired program
  The result of the process of connecting the various components in the desired configuration
© 2016 Pearson Education, Inc., Hoboken, NJ. All rights reserved.

## Slide 4
Hardware and Software Approaches
Sequence of arithmetic and logic functions
Data
Results
(a) Programming in hardware
Instruction
codes
General-purpose arithmetic and logic functions
Data
Control signals
Results
(b) Programming in software
Figure 3.1 Hardware and Software Approaches
© 2016 Pearson Education, Inc., Hoboken, NJ. All rights reserved.
Instruction interpreter

## Slide 5: Software
I/O Components
A sequence of codes or instructions
Part of the hardware interprets each instruction and
generates control signals
Provide a new sequence of codes for each new program instead of rewiring the hardware
Major components:
CPU
  Instruction interpreter
  Module of general-purpose arithmetic and logic functions
I/O Components
  Input module
    Contains basic components for accepting data and instructions and converting them into an internal form of signals usable by the system
  Output module
    Means of reporting results
Software

## Slide 6: Memory address register (MAR)
MEMORY
Specifies the address in memory for the next read or write
Memory buffer register (MBR)
Contains the data to be written into memory or receives the data read from memory
I/O address register (I/OAR)
Specifies a particular I/O device
I/O buffer register (I/OBR)
Used for the exchange of data between an I/O module and the CPU
MAR
MBR

## Slide 7
PC
MAR
IR
MBR
I/O AR
I/O BR
CPU
Main Memory
System Bus
I/O Module
Buffers
Instruction
Instruction
Instruction
Data
Data
Data
Data
0
1
2
n – 2
n – 1
Figure 3.2 Computer Components: Top-Level View
PC | = | Program counter
IR | = | Instruction register
MAR | = | Memory address register
MBR | = | Memory buffer register
I/O AR | = | Input/output address register
I/O BR | = | Input/output buffer register
Execution unit

## Slide 8: Fetch Cycle
START
HALT
Fetch Next Instruction
Execute Cycle
Execute Instruction
Figure 3.3 Basic Instruction Cycle

## Slide 9: Fetch Cycle
At the beginning of each instruction cycle the processor
fetches an instruction from memory
The program counter (PC) holds the address of the instruction to be fetched next
The processor increments the PC after each instruction
fetch so that it will fetch the next instruction in sequence
The fetched instruction is loaded into the instruction register (IR)
The processor interprets the instruction and performs the required action

## Slide 10: Action Categories
The processor may perform some arithmetic or logic operation on data
An instruction may specify that the sequence of execution be altered
Data transferred to or from a peripheral device by transferring between the processor and an I/O module
Data transferred from processor to memory or from memory to processor
Processor- memory
Processor- I/O
Data processing
Control

## Slide 11
0 3 4 15
Opcode
Address
(a) Instruction format
0 1 15
S
Magnitude
Integer format
Program Counter (PC) = Address of instruction Instruction Register (IR) = Instruction being executed Accumulator (AC) = Temporary storage
Internal CPU registers
0001 = Load AC from Memory 0010 = Store AC to Memory 0101 = Add to AC from Memory
Partial list of opcodes
Figure 3.4 Characteristics of a Hypothetical Machine

## Slide 13
Instruction address calculation
Instruction operation decoding
Operand address calculation
Data Operation
Operand address calculation
Instruction fetch
Instruction complete, fetch next instruction
Multiple operands
Return for string or vector data
Figure 3.6
Instruction Cycle State Diagram
Operand fetch
Operand store
Multiple results

## Slide 14: Classes of Interrupts
Program
Timer
I/O
Hardware failure
Generated by some condition that occurs as a result of an instruction execution, such as arithmetic overflow, division by zero, attempt to execute an illegal machine instruction, or reference outside a user's allowed memory space.
Generated by a timer within the processor. This allows the operating system to perform certain functions on a regular basis.
Generated by an I/O controller, to signal normal completion of an operation, request service from the processor, or to signal a variety of error conditions.
Generated by a failure such as power failure or memory parity error.
Table 3.1
Classes of Interrupts

## Slide 16: Transfer of Control via Interrupts

## Slide 17: Instruction Cycle with Interrupts

## Slide 18: + Instruction Cycle with Interrupts
Added to instruction cycle
Processor checks for interrupt
  Indicated by an interrupt signal
If no interrupt, fetch next instruction
If interrupt pending:
  Suspend execution of current program
  Save context
  Set PC to start address of interrupt handler routine
  Process interrupt
  Restore context and continue interrupted program

## Slide 19: Instruction Cycle with Interrupts
If any interrupt occurs the processor does the following:
  It suspends execution of the current program being executed and saves its context.
  This means saving the address of the next instruction to be executed (current contents of the program counter) and any other data relevant to the processor’s current activity.
  It sets the program counter to the starting address of an interrupt handler routine.
The interrupt handler program is generally part of the operating system. Typically, this program determines the nature of the interrupt and performs whatever actions are needed.

## Slide 21: Program Timing

## Slide 22: Instruction Cycle with Interrupts

## Slide 23: Multiple Interrupts

## Slide 24: Multiple Interrupts
Sequential Interrupt Processing
  Disabled interrupt:
  User program executing -> interrupt occurs -> disable other interrupts -> execute interrupt handler routine -> enable interrupts -> check for additional interrupts -> user program.
  Drawback: No priority for time-critical needs.
Nested Interrupt Processing
  Define priorities for interrupts
  Allow an interrupt of higher priority to cause a lower-priority
interrupt handler to be itself interrupted

## Slide 25
Priority=2
Priority=5
Priority=4

## Slide 26: I/O Function
I/O module can exchange data directly with the processor
Processor can read data from or write data to an I/O module
  Processor identifies a specific device that is controlled by a particular I/O module
  I/O instructions rather than memory referencing instructions
In some cases it is desirable to allow I/O exchanges to occur directly with memory
  The processor grants to an I/O module the authority to read from or write to memory so that the I/O memory transfer can occur without tying up the processor
  The I/O module issues read or write commands to memory relieving the processor of responsibility for the exchange
  This operation is known as direct memory access (DMA)

## Slide 27: + Interconnection Structures
Computer Modules or Components:
  Processor
  Memory
  I/O
There must be paths for connecting the modules.
The collection of paths connecting the various modules is called the interconnection structure.

## Slide 29: + Memory
Typically, a memory module will consist of N words of equal length.
Each word is assigned a unique numerical address (0, 1, …, N - 1).
A word of data can be read from or written into the memory.
The nature of the operation is indicated by read and write control signals.
The location for the operation is specified by an address.

## Slide 30: + I/O Module
I/O is functionally similar to memory. There are two operations, read
and write.
Further, an I/O module may control more than one external device. We can refer to each of the interfaces to an external device as a port and give each a unique address (e.g., 0, 1, …, M - 1).
In addition, there are external data paths for the input and output of data with an external device.
Finally, an I/O module may be able to send interrupt signals to the processor.

## Slide 31: + Processor
The processor reads in instructions and data,
writes out data after processing,
and uses control signals to control the overall operation of the system.
It also receives interrupt signals.

## Slide 32: The interconnection structure must support the following types of transfers:
Memory to processor
Processor reads an instruction or a unit of data from memory
Processor to memory
Processor writes a unit of data to memory
I/O to processor
Processor reads data from an I/O device via an I/O module
Processor to I/O
Processor sends data to the I/O device
I/O to or from memory
An I/O module is allowed to exchange data directly with memory without going through the processor using direct memory access
© 2016 Pearson Education, Inc., Hoboken, NJ. All rights reserved.

## Slide 33
B
u s
I
n
t e r c
o
n
n e c t i
o
n
A communication pathway connecting two or more devices
Key characteristic is that it is a shared transmission medium
Signals transmitted by any one device are available for reception by all other devices attached to the bus
If two devices transmit during the same time period their signals will overlap and become garbled
Typically consists of multiple
communication lines
Each line is capable of transmitting signals representing binary 1 and binary 0
Computer systems contain a number of different buses that provide pathways between components at various levels of the computer system hierarchy
System bus
A bus that connects major computer components (processor, memory, I/O)
The most common computer interconnection structures are based on the use of one or more system buses
© 2016 Pearson Education, Inc., Hoboken, NJ. All rights reserved.

## Slide 34: Data Bus
Data lines that provide a path for moving data among system modules
May consist of 32, 64, 128, or more separate lines
The number of lines is referred to as the width of the data bus
The number of lines determines how many bits can be
transferred at a time
The width of the data bus is a key factor in determining overall system performance

## Slide 35: Address Bus
Control Bus
Used to designate the source or destination of the data on the data bus
  If the processor wishes to read a word of data from memory it puts the address of the desired word on the address lines
Width determines the maximum possible memory capacity of the system
Also used to address I/O ports
  The higher order bits are used to select a particular module on the bus and the lower order bits select a memory location or I/O port within the module
Used to control the access and the use of the data and address lines
Because the data and address lines are shared by all components there must be a means of controlling their use
Control signals transmit both command and timing information among system modules
Timing signals indicate the validity
of data and address information
Command signals specify operations to be performed

## Slide 36: + Control Lines
Memory write: causes data on the bus to be written into the addressed location
Memory read: causes data from the addressed location to be placed on the bus
I/O write: causes data on the bus to be output to the addressed I/O port
I/O read: causes data from the addressed I/O port to be placed on the bus
Transfer ACK: indicates that data have been accepted from or placed on the bus

## Slide 37: + Control Lines
Bus request: indicates that a module needs to gain control of the bus
Bus grant: indicates that a requesting module has been granted control of the bus
Interrupt request: indicates that an interrupt is pending
Interrupt ACK: acknowledges that the pending interrupt has been recognized
Clock: is used to synchronize operations
Reset: initializes all modules

## Slide 38: Bus Interconnection Scheme

## Slide 39: Summary
Computer components
Computer function
  Instruction fetch and execute
  Interrupts
  I/O function
Interconnection structures
Bus interconnection
Chapter 3
A Top-Level View of Computer Function and Interconnection