## Slide 1: Computer Architecture and Logic Design (CALD) Lecture 06
+

## Slide 2: Instruction Sets: Characteristics and Functions

## Slide 3: Machine Instruction Characteristics
+
The operation of the processor is determined by the instructions it executes, referred to as machine instructions or computer instructions
The collection of different instructions that the processor can
execute is referred to as the processor’s instruction set
Each instruction must contain the information required by the processor for execution

## Slide 4: Elements of a Machine Instruction
Operation code
(opcode)
Specifies the operation to be performed. The operation is specified by a binary code, known as the operation code, or opcode
Source operand
reference
The operation may involve one or more source operands, that is, operands that are inputs for the operation
Result operand reference
The operation may
produce a result
Next instruction reference
This tells the processor where to fetch the next instruction after the execution of this instruction is complete

## Slide 5: + Instruction Cycle State Diagram

## Slide 6: Source and result operands can be in one of four areas:
Processor register
  A processor contains one or more registers that may be referenced by machine instructions.
  If more than one register exists each register is assigned a unique name or number and the instruction must contain the number of the desired register
Immediate
  The value of the operand is contained in a field in the instruction being executed
I/O device
  The instruction must specify the I/O module and device for the operation. If memory- mapped I/O is used, this is just another main or virtual memory address
Main or virtual memory
  As with next instruction references, the main or virtual memory address must be supplied

## Slide 7: + Instruction Representation
Within the computer each instruction is represented by a sequence of bits
The instruction is divided into fields, corresponding to the constituent elements of the instruction
4 bits 6 bits 6 bits
Opcode | Operand Reference | Operand Reference
16 bits
Figure 10.2 A Simple Instruction Format
Figure 12.2 A Simple Instruction Format

## Slide 8: + Instruction Representation
Opcodes are represented by abbreviations called mnemonics
Examples include:
ADD
SUB
MUL
DIV
LOAD
STOR
Add Subtract Multiply Divide
Load data from memory
Store data to memory
Operands are also represented symbolically
Each symbolic opcode has a fixed binary representation
  The programmer specifies the location of each symbolic operand

## Slide 9: Instruction Types
I/O instructions are needed to transfer programs and data into memory and the results of computations back out to the user
Test instructions are used to test the value of a data word or the status of a computation
Branch instructions are used to branch to a different set of instructions depending on the decision made
Movement of data into or out of register and or memory locations
Arithmetic instructions provide computational capabilities for processing numeric data
Logic (Boolean) instructions operate on the bits of a word as bits rather than as numbers, thus they provide capabilities for processing any other type of data the user may wish to employ
Data processing
Data storage
Data
movement
Control

## Slide 12: + Number of Addresses
3 addresses
  Operand 1, Operand 2, Result
  a = b + c;
  May be a forth - next instruction (usually implicit)
  Not common scheme
  Needs very long words to hold everything

## Slide 13: + Number of Addresses
2 addresses
  One address doubles as operand and result
  a = a + b
  Reduces length of instruction
  Common format in most architectures
  Requires some extra work
    Temporary storage to hold some results

## Slide 14: + Number of Addresses
1 address
  Implicit second address
  Usually a register (accumulator)
  Common on early machines

## Slide 15: + Number of Addresses
0 (zero) addresses
  All addresses implicit
  Uses a stack
  e.g. push a
  push b
  add
  pop c
  c = a + b

## Slide 16: + Instruction Addresses
The number of addresses per instruction is a basic design
decision.
Fewer addresses per instruction:
  less complex processor.
  instructions of shorter length.
  programs contain more total instructions
  results in longer execution times and
  longer, more complex programs.

## Slide 17: + Instruction Addresses
Also, there is an important threshold between one-address and
multiple-address instructions.
With one-address instructions, the programmer generally has available only one general-purpose register, the accumulator.
With multiple-address instructions, it is common to have multiple general-purpose registers.
This allows some operations to be performed solely on registers.
Because register references are faster than memory references,
this speeds up execution.
For reasons of flexibility and ability to use multiple registers, most contemporary machines employ a mixture of two- and three-address instructions.

## Slide 18: Instruction Set Design
Fundamental design issues: |  |  |  | 
Operation repertoire How many and which operations to provide and how complex operations should be | Data types The various types of data upon which operations are performed | Instruction format Instruction length in bits, number of addresses, size of various fields, etc. | Registers Number of processor registers that can be referenced by instructions and their use | Addressing The mode or modes by which the address of an operand is specified
Programmer’s means of controlling the processor
Defines many of the functions performed by the processor
Very complex because it affects so many aspects of the computer system

## Slide 19: + Fundamental Design Issues
Operation repertoire
  How many and which operations to provide, and how complex operations should be
Data types
  The various types of data upon which operations are performed
Instruction format
  Instruction length (in bits), number of addresses, size of various fields, and so on
Registers
  Number of processor registers that can be referenced by instructions,
and their use
Addressing
  The mode or modes by which the address of an operand is specified

## Slide 20: Types of Operands

## Slide 21: + Types of Operations
Data transfer
Arithmetic
Logical
Conversion
I/O
System control
Transfer of control

## Slide 24: + Processor Actions

## Slide 25: Data Transfer
Most fundamental type of machine instruction
Must specify:
Location of the source and destination operands
The length of data to be transferred must be indicated
The mode of addressing for each operand must be specified

## Slide 26: Arithmetic
+
Add, Subtract, Multiply, Divide
Signed Integer
Floating point ?
May include
  Increment (a++)
  Decrement (a--)
  Negate (-a)

## Slide 27: + Logical

## Slide 29: + Logical

## Slide 30: Instructions that change the format or operate on the format of data
Conversion
An example is converting from decimal to binary
An example of a more complex editing instruction is the EAS/390
Translate (TR) instruction

## Slide 31: Input/Output
+
Variety of approaches taken:
  Isolated programmed I/O
  Memory-mapped programmed I/O
  DMA
  Use of an I/O processor
Many implementations provide only a few I/O instructions, with the specific actions specified by parameters, codes, or command words

## Slide 32: System Control
Instructions that can be executed only while the processor is in a certain privileged state or is executing a program in a special privileged area of memory
Typically these instructions are reserved for the use of the operating system
Examples of system control operations:
A system control instruction may read or alter a control register
An instruction to read or modify a storage protection key
Access to process control blocks in a multiprogramming system

## Slide 33: + Transfer of Control
Reasons why transfer-of-control operations are required:
  It is essential to be able to execute each instruction more than
once
  Virtually all programs involve some decision making
  It helps if there are mechanisms for breaking the task up into smaller pieces that can be worked on one at a time
Most common transfer-of-control operations found in instruction sets:
  Branch
  Skip
  Procedure call

## Slide 34
+
Transfer of Control (Branch Instructions)

## Slide 35: Transfer of Control (Skip Instructions)
Includes an implied address
Typically implies that one instruction be skipped, thus the implied address equals the address of the next instruction plus one instruction length
Because the skip instruction does not require a destination address field it is free to do other things
Example is the increment-and-skip-if- zero (ISZ) instruction

## Slide 36: + Transfer of Control (Procedure Call Instructions)
Self-contained computer program that is incorporated into a
larger program
  At any point in the program the procedure may be invoked, or called
  Processor is instructed to go and execute the entire procedure and then return to the point from which the call took place
Two principal reasons for use of procedures:
  Economy
    A procedure allows the same piece of code to be used many times
  Modularity
Involves two basic instructions:
  A call instruction that branches from the present location to the
procedure
  Return instruction that returns from the procedure to the place from which it was called

## Slide 38: + Transfer of Control (Procedure Call Instructions)

## Slide 39: ARM Operation Types
Load and store instructions
Branch instructions
Data-processing instructions
Multiply instructions
Parallel addition and subtraction instructions
Extend instructions
Status register access instructions

## Slide 41: Summary
+
Machine instruction characteristics
  Elements of a machine instruction
  Instruction representation
  Instruction types
  Number of addresses
  Instruction set design
Types of operands
  Numbers
  Characters
  Logical data
Types of operations
  Data transfer
  Arithmetic
  Logical
  Conversion
  Input/output
  System control
  Transfer of control
ARM operation types
Chapter 12
Instruction Sets: Characteristics and Functions